SHIP INSPECTION REPORT SHIP: ‘VELLOXX’ PORT: AVONMOUTH DATE: 5TH SEPTEMBER 2013 INSPECTED BY: CAPTAIN G K SMITH Revised 08/13

2.

INDEX

Page

1.	Preamble								3

2.	General Description							3 to 4

3.	Manning								4 to 5

4.	General Inspection							5 to 12					i)	Hull

ii)	Foc'stle Head

iii)	Foc'stle Space

iv)	Main Deck Area

v)	Cargo Holds and Hatch Covers

vi)	Ballast Tanks

vii)	Accommodation Block and Poop Deck

viii)	Engine Room

ix)	Moorings and Boarding Equipment

x)	Navigation, Bridge and Communications Equipment

xi)	Navigation.

xii)	Safety Equipment

xiii)	Certification

xiv)	General

- Security								12

6.	Defects and Recommendations					13 to 14

3.

1.	PREAMBLE

On behalf of My Company Shipping Limited and My Company Shipping Limited the vessel was inspected at Avonmouth on the 5th September 2013 prior to her loading a full cargo of Wheat for Belfast.

2.	GENERAL DESCRIPTION

Name:						m.v. ‘Velloxx’

Built:						2010

Built By:					Bodewes Scheepswerven B.V. Hoogezand,  								The Netherlands.

Classification Society:			Lloyds Register (LR)

Classification:				100A1 Strengthened for Heavy Cargoes.  Containers in 						Hold and on Hatch Covers.  +LMC  UMS

Flag:	Dutch				Official Number:  5844Z G 2010	Call Sign:  PIJC

Port of Registry:  Gronginen		IMO Number:  8918591		MMSI No.  295 825 000

GRT:						2033.00 Tonnes

NRT:						1168.00 Tonnes

Summer Deadweight:			3480.00. Tonnes

Lightweight:					1217.00 Tonnes

LOA:						85.75 Metres

LBP:						79.60 Metres

Beam:						14.00 Metres

Summer Draft:				5.30 Metres

BHP:						1100.00 Kw

Bow Thruster:				No.

4.

Number of Holds:				Two  (2)

Cargo Capacity:				Grain Space:	150514 cu.ft.  /  4262.05 m3

Bale Space:	150393 cu.ft.  /  4258.62 m3

Cargo Handling Equipment:		Nil.

Last Three Voyages:  Last Cargo:	Dundee  to  Belfast			Barley

2nd Last:	Southampton  to  Belfast		Wheat

3rd Last:  	La Pallice  to  Seville			Wheat

Present Voyage:			Avonmouth  to  Belfast		Wheat

3.	MANNING

Manning Certificate Requirement:		Six  (6)

Master			Chief Engineer			2 Ratings (Certificated)

Mate							1 Rating

Actually on Board:				Seven  (7)

Officers:	Master		Chief Engineer		Ratings:	3 x AB’s

Chief Officer						Cook

Details of Certificates:

Master:  Name

Nationality:   Dutch		Certificate:  Dutch Master  No. 40900/12926  Date:  31.07.12.

Flag Certificate:  N/A

Endorsement:  As for main certificate.  Expires 31.07.17.

GMDSS Certificate:  Dutch  No. 005454  Expires 31.07.17.

SSO Certificate:  Dutch,  Groningen  Date: 06.03.14.

Medical Certificate:  26.09.13.  -  26.09.14.  (Dutch)

Mate:  Name

Nationality:  Dutch		Certificate:  Dutch Chief Mate less than 3000 grt  No. 43891/40107

Date:  07.10.12.

Flag Certificate:  N/A

Endorsement:  As for main certificate.  Expires 07.10.17.

GMDSS Certificate:  Dutch.  Expires 07.10.17.

Medical Certificate:  15.07.13.  -  15.07.14.  (Dutch)

5.

Chief Engineer: Name

Nationality:  Dutch		Certificate:  Dutch Chief Engineer less than 3000 kw.  No. 42138/947

Date:  03.09.12.

Flag Certificate:  N/A

Endorsement:  Same as main certificate.  Expires 03.09.17.

Medical Certificate:  13.01.13.  -  13.01.14.  (Dutch)

Seaman 1: Name

Nationality:  Dutch		Dutch Rating Forming Part of Navigation Watch  No. 37938/14985

Date: 26.06.02.  Expires:  02.12.23.

Medical Certificate:  23.07.13.  -  23.07.14.  (Dutch)

Seaman 1: Name

Nationality:  Portuguese	Dutch Rating Forming Part of Navigation Watch  No. 37535/66227

Date: 19.06.02.  Expires:  16.07.14.

Medical Certificate:  23.05.13.  -  23.05.14.  (Dutch)

Seaman 2:  Name

Nationality:  Cape Verde	No Watch Rating Certificate.  Has Cooks Certificate.

Medical Certificate:  10.03.13.  -  10.03.14.  (Dutch)

Cook:  Name

Nationality:  Cape Verde	Dutch Cooks Certificate.  No. G/6048/KOK  Date: 11.12.90.

Medical Certificate:  25.05.13.  -  25.05.14.  (Dutch)

4.	GENERAL INSPECTION.

i)  Hull:

Draft at time of Inspection:		2.60M For’ard  3.50M Aft

Side to the Quay:			Starboard side to.

Paintwork:	Topsides:		Generally satisfactory and well coated.  Some rust streaks 						but mainly confined to under the anchors.

Antifouling:		Some bare patches and a lot of weed.

Draft Marks etc:	Reasonable.  The Load Lines on the starboard side need 						painting white.

Fouling:	Weed			There is a lot of weed growing on the bitumastic type 						antifouling.

Barnacles:		None sighted.

Mechanical Damage:			Some minor indents all of which appear to be old damage.

ii)   Foc'stle Head:

Cleanliness:				Generally clean and tidy and free of oil or grease.

Paintwork:				All areas well coated and only isolated rust streaks.

6.

Roller Leads:				All seized.  See defects / recommendations.

Hatch to Foc'stle Space:

Ventilators:				Generally satisfactory.

Bell:					In position but requires a bell rope.

Foremast and Stays:			Generally satisfactory but the for’ard stay needs a close 					inspection.

Fire Hydrants:				Satisfactory

Rails/Bulwarks:			Satisfactory.

iii)   Foc'stle Space:

Cleanliness:				Could be cleaner and tidier.  The deck is very wet which is 						probably as a result of the Space being shut down and not 						ventilated.

Paintwork:				Fair.  All areas well coated but becoming somewhat jaded.

Fore Peak Tank Hatch:		In position and secure.

Chain Locker Access Covers:		In position and secure.

Lighting:				Satisfactory.

Emergency Generator:		Located aft and reported as fully operational.

Emergency Fire Pump:		Located aft and reported as fully operational.

Bow Thruster and Room:		Not fitted

CO2 Room:				Located aft.  Clean and tidy.

iv)   Main Deck Area:

Cleanliness:					Generally clean and tidy, free of obstructions, oil 							and grease.  Areas of light scale underneath the							paintwork in some places.

Paintwork:					All areas well coated with very few rust streaks.

Ship Side Rails/Bulwarks:			Satisfactory condition.

Watertight Doors:				None on main deck level.

Fire Hydrants:					Satisfactory condition.

Ventilators:					Satisfactory condition.

Manhole Covers to Double Bottoms:		Located in Holds except for entrance to after end 							of No.1 Hold and fore end of No.2 Hold.

v)   Cargo Holds and Hatch Covers:

Hold(s):

Condition:					In a reasonable condition consistent with a vessel							of this age.  There is a lot of light scale on the							bulkheads which is hard and no sign of it flaking 							off.

Paintwork:					Bulkheads are generally well coated.  Tank Tops 							are bare

Mechanical Damage:				No serious damage, only light damage from cargo 							operations.

7.

Access Ladders:				Reasonable condition.

Manhole Covers to Double Bottoms:		In position and secure.

Hold Bilge Wells:				Satisfactory.

Access Doors/Hatches to Hold(s):		Reasonable with dogs and hinges free and well 							greased.

Hatch Covers and Coamings:

Condition:					In a reasonable condition though there is quite a lot 							of hard scale on the underside of the hatch covers

Paintwork:					Generally in a satisfactory condition with all areas							well coated.

Rubber Seals:					There are some deep grooves forming in the								packing from compression but to date no water 							ingress has been detected.

Any signs of Hatches not being watertight:	No.

Last Hose Test:				No scheduled routine for Hose Testing or 								Ultrasonically testing the hatch covers.

Sealing Tape in use around Hatches:		No.

Condition of  Hydraulics, Wheels,		Generally satisfactory.  Some problems with the	Trackways, Quick Release Cleats etc:	hydraulics but this was repaired whilst I was on 							board.

Portable Bulkheads:				None fitted.

vi)   Ballast Tanks:

Not inspected.

vii)   Accommodation Block and Poop Deck:

Condition:			Good with the decks clear of obstructions, oil and grease.

Paintwork:			All areas well coated and clean.

Signal Mast and Stays:	Satisfactory condition.

Rails/Bulwarks:		Satisfactory condition.

Watertight Doors:		Packing good, dogs and hinges well greased.

Ventilators:			Satisfactory.

Roller Leads:			Seized.  See remarks / recommendations.

Emergency Shut Off's:		Satisfactory.

Interior Accommodation:

Galley:				Very clean and tidy.  No uncooked food lying around.

Food Storage:			Good.

Public Rooms:			Clean and tidy.

Cabins:				Clean and tidy.

Alleyways:			Clean with no obstructions.

8.

viii)   Engine Room:

Condition:				Clean and tidy.

Paintwork:				All areas well coated.

Lighting:				Satisfactory.

Plates:					Clean and free of oil and grease.

Bilges:					A small amount of oily water in them

Pipelines and Valves:			All appear to be in a satisfactory condition.

Leakages:				None sighted or reported.

Equipment:				Reported as all operational.

Oily/Water Separator:			Reported as operational.

Steering Gear:				Fully operational with no leaks.

ix)   Moorings and Boarding Equipment:

Forward:				Moderate to good.

Aft:					Moderate to good.

Spares:					Yes.

Windlass:				Operational.

Cables:					Satisfactory.

Capstan/Winch:			Satisfactory

Gangway:				Satisfactory.

Safety Net:				Satisfactory but not correctly rigged.

Accommodation Ladder(s):		Satisfactory.

Pilot Ladders:				Satisfactory.

x)   Navigation, Bridge and Communications Equipment:

Charts:						Mainly NWE and  Mediterranean.

Random check made of charts.  Satisfactory.

Notice to Mariners:				Latest Notice 34/13

'M' Notices:					None sighted.

List of Radio Signals:				2013/05

List of Lights:					2013/05

Sailing Directions:				Random check made.  Satisfactory.

Nautical Almanac:				2013  (Browns)

Tide Tables:					2013  (Browns)

Navtex:					Operational.

Navigation Tables:				Yes

Radars:					2.  Operational.

GPS:						1.  Operational

Echo Sounder:					Operational

2182 Watch Receiver:				Yes.  Operational

D.S.C. Watch Receiver:			Yes.  Operational

Radio Telephone (M.F. and V.H.F.):		Yes.  Operational

Email:						Yes.  Operational

AIS:						Yes.  Operational

9.

SSAS:						No.

Magnetic Compass:				Yes.  Last adjusted Southampton 21.06.13.

Compass Observation Book:			In deck log book.  Recent observations made.

Gyro Compass:				Yes.  Operational.

Rudder Indicator:				Yes.

Speed Indicator:				GPS

Navigation, N.U.C. and Anchor Lights:	All satisfactory.

Signal Flags:					Full set.

RPM/Speed Table:				Yes

Basic Manouvering Data:			Yes

Masters Standing/Night Order Book:		No.

GMDSS/Emergency Portable Radios:	Yes.  Three sets.  Batteries in date.

Passage Plans:					Yes.  From berth to berth.

Sextant:					Yes.

Azimuth Mirror:				Yes.

xi)	Navigation:

The vessel appears to have been navigated safely at all times with Traffic Routing systems 	complied with.

Log Book completion is of a reasonable standard.

Passage Planning is from Berth to Berth but the information regarding berth to pilot and vice 	versa in a number of cases is a bit vague.

xii)   Safety Equipment:

Liferafts:					2 x 12 man

Hydrostatic Releases:				Expire 04/14

Lifeboat(s):					Not fitted.

Rescue Boat:					Satisfactory condition.

Rescue Boat First Aid Kit:			In date.

Rescue Boat Outboard Motor:		Stowed in Funnel.

Boarding Ladders:				Satisfactory.

Pyrotechnics:					Expire 09/14.

Lifeboat Pyrotechnics:

SART's:					Expire 07/18

EPIRB:					Expire 03/15.  Hydrostatic release expires 03/15

Man Overboard Smoke Floats:		Expire 11/14 and 06/16

Line Throwing Apparatus:			Expire 10/15

Last Fire Fighting Equipment Survey:	Cork 03.06.13

Last Fixed Fire Fighting Equipment Survey:	Genoa 21.04.13.

Fire Extinguishers:				Generally satisfactory.

Emergency Fire Pump:			Reported as fully operational.

Emergency Generator:			Reported as fully operational.

Lifejackets, Survival and Immersion Suits:	Satisfactory condition.

10

Lifejacket Lights:				Expire 09/16.

Firemans Outfits:				Satisfactory.

Lifebuoys and Lights:				Good condition and lights operational.

Fire Boxes, Hoses and Nozzles:		Clean, tidy and complete.

Emergency Bells and Alarms:			Reported as satisfactory.

Emergency Lighting:				Satisfactory.

Fire Plan:					Up to date.

Emergency Plans:				Yes.

Muster Lists:					Up to date.

Safety Signs etc:				Yes.  Satisfactory.

Emergency Steering:				Last full test from Steering Flat 22.07.13	Emergency Drills:				Fire Drill 02.08.13

Boat Drill 10.08.13.

Rescue at n Water 10.08.13.

SOPEP Drill 18.08.13.

Abandon Ship Drill 25.08.13.

Solas Manual:					Yes.

Bridge Watchkeepers Alarm:			Yes.  Fully operational.

xiii)   Certification:

Survey Due     Last Survey     Cert.Issued

Register	2085/2013			01.03.18.			01.0313.

Certificate of Class				22.03.17.	19.03.12.	01.05.12.

Interim Certificates of Class					Beverwijk	19.03.13.

Load Line Certificate				22.03.17.	19.03.12.	12.04.12.

Safety Construction Certificate		22.03.17.	19.03.12.	12.04.12.

Safety Equipment Certificate			22.03.17.	19.03.12.	12.04.12.

IOPP Certificate				22.03.17.	19.03.12.	12.04.12.

Certificate of Seaworthiness:			22.03.17.			12.04.12.

International Ship Security Certificate:	20.05.19.	20.05.13.	27.05 13.

Continuous Synopsis Record:							Yes

Suez Canal Tonnage Certificate:						No.

Panama Canal Tonnage Certificate:						No.

# Safety Radio Certificate			22.03.17.	19.03.12.	12.04.12.

Radio Licence									20.03.10.

GMDSS Maintenance Contract						Displayed

Hull Special Survey				22.03.17.

Drydocking

Tailshaft Survey				     03.07.

Accommodation Certificate:			22.03.07.			12.04.12.

Derat Certificate				07.01.15.	07.07.13.	07.07.13.

Liferafts Certificates				26.04.15.	26.04.13.	26.04.13.

Rescue Boat Certificate			Not sighted

HRU Certificates:				     04.15.

11.

Survey Due	Last Survey	Cert.Issued.

Certificate for Testing Rescue Boat Falls:					Not sighted

Rescue Boat Wire:					(Turned 25.03.13.)	25.04.10.

Free Fall Lifeboat Certificate:							N/A

Certificate for Testing Free Fall Boat:					N/A

Register/Cert. Of Lifting Gear Tests:						No.

Flag Sate Inspection								10.04.13.

Medical Locker Replenished:			08.07.12			08.07.13.

International Tonnage Certificate						18.09.10.

Safe Manning Certificate			22.03.17.			21.06.12.

Grain Carrying Certificate			22.03.17.	19.03.13.	12.04.12.

Timber Carrying Certificate							No.

Carriage of Bulk Cargoes:							22.03.10.

Carriage of Dangerous Goods							No.

DOC Certificate:  (Office)			06.11.16.	15.12.12.	06.11.10.

Safety Management Certificate:		26.04.17.	26.04.12.	26.04.10.

Certificate of Financial responsibility						No

SOPEP									28.02.10.

xv)   General:

Articles of Agreement:		Record kept of Crew changes.

Official Log Book:			Incorporated in Deck Log Book.

Oil record Book:			Last entry 04.09.13.

Last Receipt for Discharge Ashore:	Corunna 24.08.13.

Garbage Book:			Last entry 04.09.13.

Last Receipt for Landing of Garbage: AVONMOUTH  04.09.13.

Trim and Stability Information:	Approved 07.04.11.

Cargo Securing Manual:		Approved 30.03.11.

Cargo Record Book:			Up to date.

Fleet Order File:			As per Northern Ship Management’s ISM

ISM Safety Management Manual:	Northern Ship Management.

Alcohol Testing Kits:			No.

Deck Log Book:			Satisfactory

Engine Room Log Book:		Satisfactory.

GMDSS Log:				Up to date and recording test calls.

Previous Port State Inspection

19.02.12.	Cork		NIL

31.03.12.	Villagarcia	NIL

30.07.12.	Lowestoft	Certificates for Radio Personnel

Rescue Boat launching.

Fire Fighting Appliances manual incomplete.

Steering Gear Emergency Preparedness.

12.

07.10.12.	Setubal		ISM / Emergency Preparedness

Emergency Manual incomplete.

17.02.13.	Dublin		NIL

21.07.13.	Southampton	Emergency Fire Pump does not start

Crew cannot demonstrate GMDSS DSC equipment in operation.

OWS operation cannot be demonstrated.

No precise information to ship about quantity and stowage factor 					of cargo prior to loading

Records of rest for Master missing.  Chief Officer 3 times in 					violation of rest requirements in July.

ISM Manual not up to date.

Radio Log not filled in for several days in July and after August 					16th no Test Calls recorded

MH/HF Test call could not be demonstrated.

Port repeater and Steering repeater not in line.

Display of GPS in parts not readable.

Deviation Table older than 2 years.

Safety fuse on bridge of portable extinguisher missing.

Rescue Boat engine locked in funnel – no key on site.

Hatch Cover / Coaming drain pipes not fitted with non-return					valves.

Light in Emergency Escape Port Side forward n Engine Room not 					working.

Engine Room Bilge aft full of 30 cms. oily bilge water

MH/HF transmitting aerial in very poor condition.

MF/HF transmitter power output unsatisfactory – less than 50%

5.	SECURITY

In general security on the vessel was reasonable with most areas locked and secured.

The one major defect was that when I boarded the vessel no one asked me for any identification or asked to search my bag.

Training drills have been carried out as per schedule.

Contacts with the ports have been made regarding details of the PFSO.  With reference to Avonmouth the vessel was still waiting for information regarding the PFSO and had been in the port for some 15 hours.

The crew were aware of what Security Level the vessel was on.

There have been no threats to the vessel.

13.

6.	DEFECTS AND RECOMMENDATIONS

| No. | Date | Defects / Recommendations | Completed |
| --- | --- | --- | --- |
| 1. 2. 3. 4. 5. 6. 7. 8. 9. 10. 11. 12. 13. | 05.09.13. | 2 of the sailors had Rating Forming Part of Navigation Watch Certificates. The third one, did not having I understand previously sailed as Cook. Under the Manning Certificate on board it is possible he does not need one but this should be clarified. The for’ard leading foremast stay is becoming very rusty at the lower end and needs a close inspection. Possibly it will need renewing. All the roller leads are seized. I was advised that these are never used and the only ones used for mooring are the enclosed panama type leads. There is quite a lot of weed on the Hull covering the area that is coated with a bitumen like substance. The Load Lines need painting. The Hull has recently been painted but this is still to do. The Rescue Boat Engine is kept in the Funnel. There is no sign in the Boat or near vicinity to say where it is kept. There is no record of the Hatches being Hose Tested or Ultrasonically tested. The packing on the Hatches is beginning to have fairly deep grooves in it. I was advised that to date there is no sign of any water ingress through the hatches. There is no Masters Standing / Night Order book in use. I was advised that since there is only the Master and Mate as Watchkeepers it was not considered necessary. By the time I left the vessel she had been alongside for 15 hours and had still not received any information from the port as to who the PFSO was. Security on board was reasonable with all entrances etc. locked. However I was not asked for any identification when I boarded the vessel nor was my bag searched. The latest list of the National Operational Contact Points (30.06.13.) was not on board. There is no photocopier on board the vessel. |  |

14.

| No. | Date | Defects / Recommendations | Completed |
| --- | --- | --- | --- |
| 14. 15. 16. 17. 18. | 05.09.13. | The IMO number is painted on the stern. It has not been cut into the Hull though I understand it is planned to do it at the next docking. Also the size of the lettering needs to be checked as it looks smaller than the dimensions given in the ISPS Code. Paint is being stowed in the Foc’stle Space though there is no Sprinkler System fitted. In the Passage Planning the details for the passage between the berth and pilot station and vice versa are on a number of occasions a bit vague. The gangway net was not rigged correctly. There are no alcohol testing kits on board. |  |